## Slide 1: Design and Implementation of Smart Farming
Supervisor: Prof. Dr. Chaiyod Pirak
IoT– Project Proposal
Group 2 - Hafsa Murtaza, Narmeen Falak

## Slide 2: Contents
Conceptual Design
Features
System Components
Hardware Connection
Software Flowchart
Task Distribution
Project Timeline

## Slide 3: Conceptual Design
Mini DC Water Pump
DHT11 as Temperature and Humidity Sensor
NodeMCU – ESP8266
Water pipe from pump outlet
Sensor will be put inside the plant
Display Results on Freeboard
Notify on Mobile Application
LCD Display

## Slide 4: Features
Real Time Measurement
  Temperature of the surroundings
  Humidity of the surroundings
  Soil Moisture of the Plant
Real Time Display
  Temperature of the surroundings
  Humidity of the surroundings
  Soil Moisture of the Plant
  Water Pump On/Off Status
Data logging
  Maximum 1000 samples
  sample interval – every 60 mins

## Slide 5: Features (Cont)
Water pump is controlled by a manual control and an automatic control (depending on soil moisture)
Send alert notification on mobile application if temperature, humidity or soil moisture is not in optimum limits
Send alert notification when water pump is turned on and when water pump is turned off.

## Slide 6: System Components
The MCU: ESP8266
Mini Water Pump DC 3-6V 3W
Humidity sensor DHT11
Temperature sensor DHT11
Soil Moisture sensor
LCD Display (16*2 or 20*4)
Water pipe (inlet to pump; 5mm)
Water pipe (oulet from pump; outer dia 7.5mm, inner dia 4.5 mm )

## Slide 7: Software Flowchart

## Slide 8: Software Features
Display humidity, temperature, soil moisture and pump status on mobile app
Enable user to control pump through mobile app
If temperature > upperLimitor || temp < lowerLimit send notification
If humidity > upperLimit || humidity < lowerLimit: send notification
If soil moisture < lowerLimit: turn on pump
If soil moisture >= threshold: turn off pump
If soil moisture > upperLimit: send notification

## Slide 9: Software Features/Modules
Function: MeasureTemp
  Input: measurement unit ( Celcius ), output: temperature value
Function: SendTempNotification:
  Input: temperature value, minimum/maximum allowed temperature
Function: MeasureHumidity
  Input: measurement unit ( percentage), output: humidity value
Function: SendHumidityNotification:
  Input: humidity value, minimum/maximum allowed humidity
Function: MeasureSoilMoisture:
  Input: measurement unit (bars), output: soil moisture value
Function: RegulateMoisture:
  Input: desired moisture value
Function: SendMoistureNotification:
  Input: current moisture value, maximum/minimum allowed moisture values
Function: UpdateDisplay
  Input: temperature, humidity, soil moisture and water pump status

## Slide 10: Task Distribution
Hafsa:
Narmeen:

## Slide 11: Timeline
Task | Week |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Requirements and Design Finalization | x | x |  |  |  |  |  |  | 
Hardware purchase and Implementation |  | x | x | x |  |  |  |  | 
Software Implementation |  |  |  | x | x | x |  |  | 
Testing |  |  |  |  |  | x | x | x | 
Documentation |  | x |  | x |  | x | x | x | 
Delivery |  |  |  |  |  |  |  |  | x

## Slide 12: Additional (If necessary):
Using ML (regression) on the saved data
And extrapolating it further to predict the least Moisture beforehand so as to get the water for the next cycle ready.